## Slide 2: Spinlock

## Slide 3: SMP keys
Kernel synchronization
  Spinlock is one of synchronization mechanisms. It uses exclusive load/store.
    ARM: Exclusive load/store needs cache to be on.
Cache coherence
  ARM: SCU/L2 controls

## Slide 4: Spinlock
p0
p1
Critical region
p0
p1
Using Spinlock
spin_lock
spin_unlock

## Slide 5: Cache coherence
L2 (with snoop logic)
C0
C1
Cache coherence
Write
Update to the cache line that has the same phy address

## Slide 6: Kernel synchronization#1
Technique | Description | Scope
Per-CPU variables | Duplicate a data structure among the CPUs | All CPUs
Atomic operation | Atomic read-modify-write instruction to a Counter | All CPUs
Memory barrier | Avoid instruction reordering | Local CPU or All CPUs
Spin lock | Lock with busy wait | All CPUs
Semaphore | Lock with blocking wait (sleep) | All CPUs
Seqlocks | Lock based on an access counter | All CPUs
Local interrupt disabling | Forbid interrupt handling on a single CPU | Local CPU
Local softirq disabling | Forbid deferrable function handling on a single CPU | Local CPU
Read-copy-update (RCU) | Lock-free access to shared data structures through pointers | All CPUs

## Slide 7: Kernel synchronization#2
Kernel control paths accessing the data structure | UP protection | MP further protection
Exceptions | Semaphore | None
Interrupts | Local interrupt disabling | Spin lock
Deferrable functions | None | None or spin lock
Exceptions + Interrupts | Local interrupt disabling | Spin lock
Exceptions + Deferrable functions | Local softirq disabling | Spin lock
Interrupts + Deferrable functions | Local interrupt disabling | Spin lock
Exceptions + Interrupts + Deferrable functions | Local interrupt disabling | Spin lock

## Slide 8: Kernel synchronization#3
Deferrable functions accessing the data structure | Protection
Softirqs | Spin lock
One tasklet | None
Many tasklets | Spin lock

## Slide 9: ARM’s swap instruction#1
swap instruction
  an “atomic” instruction across CPUs that will block BUS.
  swap a word between memory and a register
Using swap to implement semaphore MOV r1, =semaphore MOV r2, #1 SWP r3, r2, [r1] ; hold the bus until complete CMP r3, #1 BEQ spin

## Slide 10: ARM’s swap instruction#2
Lock
Core 0
Core 1
0
1
1
①
1
0
1
②
1
0
1
③

## Slide 11: ARM’s exclusive load/store
Exclusive load/store starts from ldrex and ends at strex. The whole process won’t block BUS.
strex can tell if the exclusive load/store operation succeeds.

## Slide 12: spin_lock#1
p0
p1
2 load/store pairs overlay
ldrex
strex
ldrex
strex

## Slide 13: spin_lock#2
spin_lock static void spin_lock(spinlock_t *lock) { unsigned long tmp; unsigned int lockval; LOCK_LOOP: __asm { ldrex lockval, [&lock->slock] cmp lockval, #0 bne LOCK_LOOP add lockval, #1 strex tmp, lockval, [&lock->slock] teq tmp, #0 bne LOCK_LOOP dmb } }
spin_unlock static void spin_unlock(spinlock_t *lock) { unsigned int tmp; __asm { mov tmp, #0 dmb str tmp, [&lock->slock] } }
Spinlock has been acquired by some process
ldrex/strex operation has been interfered

## Slide 14: 不會卡住
static inline void arch_spin_lock(arch_spinlock_t *lock) { unsigned long tmp; __asm__ __volatile__( "1: ldrex %0, [%1]\n" " teq %0, #0\n" WFE("ne") " strexeq %0, %2, [%1]\n" " teqeq %0, #0\n" " bne 1b" : "=&r" (tmp) : "r" (&lock->lock), "r" (1) : "cc"); smp_mb(); }
static inline void arch_spin_unlock(arch_spinlock_t *lock) { smp_mb(); __asm__ __volatile__( " str %1, [%0]\n" : : "r" (&lock->lock), "r" (0) : "cc"); dsb_sev(); }
Core A
Core B
以下為補充資料，純屬推測，需要再確認。

## Slide 15: 會卡住 #1
static inline void arch_spin_lock(arch_spinlock_t *lock) { unsigned long tmp; __asm__ __volatile__( "1: ldrex %0, [%1]\n" " teq %0, #0\n" WFE("ne") " strexeq %0, %2, [%1]\n" " teqeq %0, #0\n" " bne 1b" : "=&r" (tmp) : "r" (&lock->lock), "r" (1) : "cc"); smp_mb(); }
static inline void arch_spin_unlock(arch_spinlock_t *lock) { smp_mb(); __asm__ __volatile__( " str %1, [%0]\n" : : "r" (&lock->lock), "r" (0) : "cc"); dsb_sev(); }
Core A
Core B

## Slide 16: Real wfe #2
static inline void arch_spin_lock(arch_spinlock_t *lock) { unsigned long tmp; __asm__ __volatile__( "1: ldrex %0, [%1]\n" " teq %0, #0\n" WFE("ne") " strexeq %0, %2, [%1]\n" " teqeq %0, #0\n" " bne 1b" : "=&r" (tmp) : "r" (&lock->lock), "r" (1) : "cc"); smp_mb(); }
static inline void arch_spin_unlock(arch_spinlock_t *lock) { smp_mb(); __asm__ __volatile__( " str %1, [%0]\n" : : "r" (&lock->lock), "r" (0) : "cc"); dsb_sev(); }
Core A
Core B